## Slide 1
GENERAL ALIGNMENT DRAWING – PROPOSED 4 KM DRAINAGE AT CAMP-18 UKHIA
NOTE: ORIGINAL CONTENT OF THE MAP IS TAKEN FROM IOM AS PER THE DETAIL PROVIDED IN THE SHEET | 
CHECKED BY – KHAIRUL BASHAR- WASH MANAGER PMO | 
NOTED BY – SANJAY MUKHERJEE- PC– GERMAN RED CROSS | 
DATE-03032020 | 
DRAWING NO- UC18DN1 | 
MAP OF THE PROPOSED LOCATION BY SMSD
CAMP BOUNDARY
BLOCK BOUNDARY
SUB-BLOCK BOUNDARY
CiC OFFICE
SUB-PROPOSED DRAIN CONSTRUCTION BY BDRCS/GERMAN RED CROSS

## Slide 2
PART PLAN OF PROPOSED SURFACE DRAIN
565 mm
565 mm
305 mm
Wide Drain
130 mm Brick work with plaster
130 mm Brick work with plaster
A
A’
PART SECTION A-A’ OF PROPOSED SURFACE DRAIN
100 mm PCC Bed
305 mm
Brick work
(Average Hight)- to be adjusted as per site topo
GENERAL SPECIFICATION
All Brick Work shall be first class.
All plain cement concrete shall be of ratio 1:2:4
All Cement Plater work Shall be of ratio 1:4
Excavation Work shall be compacted to desired level as directed site engineers in-charge
PCC Bed shall be laid On plastic apron of standard quality approved by site engineer.
In some places have to construct 255mm (10”) thick brick work based on alignment as per the direction of Engineer in-charge.
Plastic Sheet Apron for protecting PCC seepage during construction
305 mm
Wide Drain
GENERAL ARRANGEMENT DRAWING – PROPOSED 4 KM DRAINAGE AT CAMP-18, UKHIA
DRAWN BY – ZAHIRUL ISLAM- SPO – ENGINEER- GERMAN RED CROSS | 
CHECKED BY – KHAIRUL BASHAR- WASH MANAGER PMO | 
NOTED BY – SANJAY MUKHERJEE- PC– GERMAN RED CROSS | 
DATE-03032020 | 
DRAWING NO- UC18DN2 | 
Compact Soil Foundation